Tardygrade BOM
Apart from the Tardygrade PCB and 3d printed parts, this is the complete list of components needed to build the robot.
I usually include the exact web store links from where I bought each component. Since I sourced my parts locally from Sweden these are mainly for reference. You should get the components from wherever is convenient from your location.

ESP32 dev board
Qty.	Alt.	Part	Description
1	A	Adafruit Feather HUZZAH32 – ESP32	https://www.adafruit.com/product/3405
	B	TinyPICO	https://www.tinypico.com/ / Webstore link (Tindie)
	C	If you happen to have a TinyS2 board, that should work too. / Seems like it’s not currently for sale though.

Miscellaneous parts
Qty.	Part	Description
1	3.7V lipo cell / 1500 mAh / Type 803450	Dimensions: 8 x 34 x 50 mm. / You can also use any cell smaller than that. / https://www.electrokit.com/produkt/batteri-lipo-3-7v-1500mah/
1	JST-PH connector extension cable	Length: ~150 mm / Wire diameter: 1.2 mm (max) / https://www.electrokit.com/produkt/kabel-med-vinklad-kontakt-jst-ph-2-pol-150mm/
1	Micro servo 360° continuous rotation	“Tower Pro 9g” form factor / https://www.electrokit.com/produkt/servo-msr-1-3-9-360/
1	Micro servo 180° rotation	https://www.electrokit.com/produkt/mg90s-micro-servo/ / (The link shows a metal gear servo, but nylon gears works just as well)
1	Neodymium magnet	Dimensions: 6 x 3 mm / Webstore link (Amazon)

PCB components
Through-hole
Qty.	Part	Description
2	Electrolytic capacitor 220 µF	Exact value not important for this part.
1	Male pin header 1 x 40, right angle / 2.54 mm	https://www.electrokit.com/produkt/stiftlist-2-54mm-1x40p-vinklad-brytbar/
1	Female pin header x 40 / 2.54 mm	https://www.electrokit.com/produkt/hylslist-2-54mm-1x40p/
1	Pushbutton off-(on) / 2.54 mm	Optional. Needed for older TinyPICO boards with no onboard reset button. / https://www.electrokit.com/produkt/skhlaba010-omkopplare/
1	Switch on-on / 2.54 mm	Optional. Used only with Adafruit board to power down its boost regulator. / https://www.electrokit.com/produkt/skjutomkopplare-1-pol-on-on-pcb-2/
Surface mount
Qty.	Part	Description
2	P-channel MOSFET / Logic level / Package: SOT-23	Gate-Source Threshold: < 3V / Rds On: (The lower the better) / I used this one: Datasheet
1	Resistor 200Ω / Package (in): 0603
1	Resistor 10kΩ / Package (in): 0603
1	Boost regulator, / Microchip MCP1642B/D	There are two variants, named B and D. / They are interchangeable for this application. / Datasheet
2	Ceramic capacitor, 10 µF / Package (in): 0603	Refer to MCP1642B/D datasheet section 5.4 for details on cap selection. / I used this one: Webstore link (Mouser)
1	Inductor, / Wurth 744052005	If you can’t source this part, the MCP1642B/D datasheet table 5-2 lists other suitable inductors. / Webstore link (Mouser)
4	Hall switch, / Diodes AH1815-W-7 / Package: SOT-23	This part might be hard to source currently. / Good luck! / Webstore link (Mouser)
4	Ceramic capacitor, 10 nF / Package (in): 0603	Webstore link (Mouser)

Revision history
Rev.	Date	Comment
1	2021-09-21